SMOG

The SMOG program is a FORTRAN program, which simulates LA style smog.  Although the program includes a number of simplifications, the results are approximately correct and are quite instructive.  The basic method is similar to that used in much more complex smog models.  The program works by calculating an A (source) term and B (loss) term from 36 rate equations and then stepping the concentrations forward by numerically solving the equation:

dX/dT = A  -  B  *  X

where A = sum of all source rate terms; B = sum of all first order loss processes and X is the compound of interest.  The program approximates each concentration X at time t+1  as:

X(t+DDT) = X(t) + A*DDT/(1.0 + B*DDT)

where: DDT is the integration step interval.  This is an approximate solution to the differential equation given above.  An exact solution to this diff. eq. is:

X(t+dt)= A/B + (x(t)-A/B)*exp(-B*dt)

However since exponentials are slow on PCs the exponential is approximated as: exp(X) = 1+X which is valid for x<<1.  Advection in and out of the box is simply treated as another source or loss of X.  The advection loss is input as a wind speed in m/second and is used assuming a 10x10 km box.  All calculations and output data in the program are in mixing fraction units.  The sun turns on each day at 6 am and sets at 6 pm (THINJ), however since some reactions need shorter wavelength light they only occur during the mid-day hours (THICKJ).  During each reporting interval, 6 integration steps are undertaken.  So, for a 0.25 hour reporting interval (15 minutes) the A and B terms are updated every 2.5 minutes (15/6).  In addition there is a simple wind removal of pollutants in the box, which depends on wind speed.  To run the program, simply type SMOG or click on SMOG.exe from the windows file manager.  Although the program is a DOS based program, it runs fine from windows. You could also port the smog.for program to another environment (like a Unix machine), then compile and run it there.  The results should be identical.  The program will ask for QNO and QHC in units of ppbv/second, a number of days, a wind speed and an output file name (use a name like XXXX.DAT.  If this file already exists it may overwrite it without warning.  The Q sources are in units of ppbv/sec (in the whole box).  Start with the base case: QNO=0.003, QHC=0.015, #days=2, wind speed =1

The following files are used to run the program:

SMOG.FOR  The FORTRAN source code.

SMOG.EXE 	The executable file.
SMOG.DOC 	The WORD version of this document.

SMOG.XLS   An Excel Spreadsheet template for looking at the results and graphing

The program considers some 36 reactions on 19 different compounds.  Source fluxes of HC's, and NO are input parameters, but the daily pattern is fixed at 100% of the input from the hours of 6-9 am and 4-7 pm, 40% from 9am -4pm and 7pm -midnite, and 10% at other times.  The flux of CO is fixed at 10 times the HC flux and NO2 is 10% of the NO flux.  Note that the hydrocarbon chemistry in this model is simulated with only one generic hydrocarbon.  This is a significant simplification which would need to get changed before this model could be used for research or policy decisions.

The gaseous species considered are:

1; O3P	2; O1D	3; O3	4; NO	5; OH	6; HO2

7; CO	8; HCO	9; H2CO	10; CH3	11; CH3O	12; CH302

13; H	14; NO3	15; H2O2	16; NMHC 	17; NO2	18; N2O5

19; HNO3

The reactions considered are:

1;	NMHC  + OH  =  CH3  +  HOH

2;	M  +  CH3  +  O2  =  CH3O2

3;	CH3O2  +  NO  =  CH3O  + NO2

4;	CH3O   +  O2  =  H2CO  +  HO2

5;	H2CO   +  HV  =  HCO   +  H

6;	M  +  H  +  O2   =  HO2

7;	HCO  +  O2   =  CO  +  HO2

8;	CO   +  OH  + O2  =  CO2  +  HO2

9;	NO   +  HO2  =  NO2  +  OH

10;	NO2  +  HV   =  NO   +  O (3P)    R(10) reaches a maximum of 0.01 sec-1 at noon

11;	M   +  O (3P)  +   O2  =  O3

12;	O3  +  HV  =   O2  +  O(1D)         R(12) reaches a maximum of 5.5E-6 sec-1 at noon

13;	O (1D)  +  M  =  O (3P)

14;	0 (1D) +  HOH  =  2 OH

15;	OH  +   HO2  =  HOH  +  O2

16;	NO  +   O3  =  NO2  +  O2

17;	OH  +   O3  =  O2   +  HO2

18;	HO2  +  O3  =  2O2  +  OH

19;	NO2  +  O3  =  NO3  +  O2

20;	NO3  +  HV  =  O (3P)  +  NO2

21;	O3  +  HV   =   O2  +  O (3P)

22;	H2CO   +   HV   =  CO   +   H2

23;	NO3  +  NO   =   2 NO2

24;	H2CO  +  OH  =  HOH   +  HCO

25;	2 HO2   =   H2O2  +  O2

26;	H2O2   +  HV   =  2 OH

27;	H2O2   +  OH   =  HOH  +  HO2

28;	O (3P)  +  O3   =  2 O2

29;	O (3P)  +  HO2  =   O2  +  OH

30;	O (3P)  +  H2CO  =  HCO  +  OH

31;	O  +  NO2  =  O2  +  NO

32;	M  +  OH   +  NO2   =   HNO3

33;	M  +  NO2  +  NO3   =   N2O5

34;	N2O5  +   HV   =   NO3   +   NO2

35;	OH  +   HNO3   =   HOH   +  NO3

36;	HNO3   +  HV   =   OH  +  NO2

Rate constants are given below.  Units are as follows:

Sec-1 for first order reactions;  atm/sec for second order reactions.

To convert second order rate constants into cm3/molecule*sec multiply by 4.06E-20

| R(1)=1.4E+9 | R(2)=3.25E+7 | R(3)=1.4E+7 | R(4)=6.5 | R(5)=8.0E-4 | R(6)=2.375E+6 |
| --- | --- | --- | --- | --- | --- |
| R(7)=2.85E+7 | R(8)=3.5E+6 | R(9)=2.025E+8 | R(10)=1.0E-2 (noon) | R(11)=8.0E+4 | R(12)=5.5E-6 (noon) |
| R(13)=7.25E+8 | R(14)=5.75E+9 | R(15)=7.5E+8 | R(16)=3.0E+5 | R(17)=1.1E+6 | R(18)=2.025E+4 |
| R(19)=5.25E+2 | R(20)=5.0E-2 | R(21)=1.0E-3 | R(22)=1.8E-6 | R(23)=4.75E+8 | R(24)=3.0E+8 |
| R(25)=6.25E+7 | R(26)=1.6E-6 | R(27)=1.775E+7 | R(28)=1.4E+5 | R(29)=8.75E+8 | R(30)=3.0E+6 |
| R(31)=1.475E+8 | R(32)=1.625E+9 | R(33)=1.75E+9 | R(34)=3.75E+6 | R(35)=1.0E-3 | R(36)=1.0E-4 |

The water mixing ratio is fixed at 1% and the pressure is fixed at 1 atm.

Once the results are calculated a rather large and unwieldy data set is obtained.  However the results can be directly input into an Excel spreadsheet that I have already set up by following the following directions:

To load the results into Excel:

1) Start Excel and open the file “Smog.xls”.  This is a template which has the columns and two graphs pre-defined for the smog data;

2) Open a second file which is the data file.  It is necessary to use “comma delimited” format so that the numbers line up correctly in the spreadsheet;

3) Copy the entire page of numbers from the new spreadsheet to the smog.xls page;

When copying them into smog.xls if you put the cursor into block “B3” the columns will all line up and the "A" column will give you a nice time axis.

4) Once this is done, you can easily look at your data.  Several graphs have been predefined for you and are on separate pages of the spreadsheet.

This weeks problem set is as follows: Use the results for the base case given above (QNO = 0.003; QHC = 0.015, V=1m/s) to answer the following questions.

1) CO, with a lifetime of about a month, is essentially an inert tracer.  When does it peak and why?  From the calculated CO time series and the source flux (Qco=10*Qhc), determine the advection time that the model is using (note, it's around 3 hrs)  Don't forget that the source flux varies with the time of day.  In other words, for a 10x10 km box and knowing the source flux, show how to calculate the wind speed.

2) From 0000-0600, why does CO increase during the first day, but decrease during the second?

3) Do calculations for the base case emissions, but with variable wind speeds.  Consider the range from around 0.2 or 0.3 to about 10 m/s.  Plot the maximum CO and O3 vs wind speed.  Are the two plots linear?  If not, can you plot them some other way which might give a linear relationship.  Why?

4) Plot the CO and hydrocarbon concentrations vs time on one graph.  Explain the similarities and the differences.

5) OH is produced from the photolysis of O3.  Yet in the model run the OH maximum precedes the O3 maximum.  In quantitative terms explain what is happening.  Which reactions are most important to explain this?

6) Compare the noontime NO/NO2  ratio calculated by the model to that from the Leighton relationship?  (Note k for the NO + O3 reaction in the model is 1.2E-14 cm3/molecule*sec and J-NO2 at noon is 0.01 sec-1.  Explain any differences.

Calculate the max O3 concentration in 16 model runs with varying emission factors. Report your results in a 4 x 4 matrix where each square of the matrix contains the maximum ozone concentration in ppb and the hour for the maximum O3 for a 2 day run.  Put the "base" case(QNO = 0.003 and QHC = 0.015) in the middle of your matrix and vary the input amounts larger and smaller than these. For all cases, use a wind speed of 1 m/s.  The maximum ozone concentrations are typically found during the afternoon hours, though not always. In your most extreme case, use a source term of one order of magnitude above and below the base case, beyond this the results quickly become meaningless.  Choose your emission values to find the HC/NOx ratio which gives the "optimum" ozone production in this model.

Answer the following questions about your model, by using the base case and the QNO/QHC ratio as a guide:

7)In your highest NOx/HC cases (large QNO/QHC) when is the ozone maximum and why?

8)In one of the runs which generate large ozone concentrations, when is the ozone maximum and why?

9)What NOx/HC ratio makes for optimum ozone production in this model?  How does this result compare with other photochemistry models ?  (e.g. Figure 4.9, pg 101 in the Jacobson text or Turco, Fig 6.12, pg 159 or Finlayson-Pitts and Pitts pg 882).  Do you get a similar result?  Why do you get this rather surprising behavior?

B.J. Finlayson-Pitts and J.N Pitts.  Chemistry of the Upper and Lower Atmosphere. Academic Press, 2000.

R.Turco. Earth Under Siege. Oxford Press, 1997.