## Slide 1: Quantum Dots in Solar Cells
Hugh Higinbotham

## Slide 2: Photovoltaics (PVs)
Convert light to electric current
GHG neutral energy source
Currently cheaper than coal/natural gas on the utility scale, but not efficient enough to be do well in current energy market
  Huge demand for more efficient and/or easier to manufacture technologies

## Slide 3: Semiconductor Review
https://commons.wikimedia.org/wiki/File:Semiconductor_band_structure_(lots_of_bands_2).svg
(Uhl 2016)
ni
Notes: Bands: extension of molecular orbitals to a crystal, become bands (chalk talk if needed), describes electron energies
Valence band: highest energies occupied at T= 0
Band gap = impossible energies
EXTRA NOTES IF MORE DETAIL NEEDED:

## Slide 4: Semiconductors in PV
https://en.wikipedia.org/wiki/P%E2%80%93n_junction
Junction (e.g. p-n) creates potential gradient causing current to flow after photon absorption
(Uhl 2016)
Notes: Photon excites electron from valence band into conduction band
  Resulting electron-hole pair (exciton) contributes to current at pn junction
  P vs N: “dope” with different impurities that increase number of charge carriers of a given type, donor for N, acceptor for P. Donors have more valence electrons
  Fermi Level increases for N, decreases for P, so when matched at junction bands bend

## Slide 5: Energy Losses
Resistive
Reflection
Transmission,
absorption
Thermalization
Recombination
Schulze et al., Energy Environ. Sci.,2015, 8,103
Notes: Accompany with reference to previous figure and a small bit of chalk talk (fill factor)
Way to minimize losses beyond theoretical limit is to couple diff. technologies to utilize parallel absorption and/or diff. bandgaps
Max theoretical limit (given some conditions like single-junction) is Shokley-Quaiser Limit, 34%

## Slide 6: Thin Film PVs
Todorov et al., Prog. Photovolt. (2013) 21, 82-87
Notes: Most new PVs involve thin semiconductor films: lots of potential for mass fabrication and precise bandgap engineering
Slide is largely for the sweet pic

## Slide 7: Quantum Dots
Engineering Bandgaps to create different potentials (e.g. finite square well)
Surround low bandgap nanocrystal with higher -> “artificial atom” Discrete energy levels, closer spaced for larger dot
(Riel 2008)
Notes: Figure: show creating of potential well by matching bandgaps, then generalize to 2D and 3D with quantum wire and quantum dot
Also surprising property that multiple electrons can be excited by a single photon, mysterious mechanism

## Slide 8: QDPV Types
Metal-Semiconductor (Schottkey) Junction
Polymer-Semiconductor
Semiconductor-Semiconductor
  QDSSC
(Kamat 2008)
Notes: 3 Main schemes for using QDs in solar cells: differences lie in engineering bandgaps, energy landscapes of junctions, and manufacturing requirements of different materials

## Slide 9: Experiments
Experimental work in classifying QD mixes and their properties in actual PVs
(Kamat 2008)
(Riel 2008)
Notes: Building small cells and measuring efficiencies as well as creating thin films and classifying, lots of imaging and spectroscopy (UW MAF (molecular analysis facility)
Riel: Self-assembly quantum dots under scanning electron microscope
Kamat: a) Schematic of conductive AFM b) AFM height image of spin-coated film c) Photocurrent map under illumination w/0 external voltage

## Slide 10: Schottkey-Junction Cells
(Kamat 2008)
Band bending only occurs in large metal-semiconductor junctions
Get improved energetics in nanoparticles with Fermi-level equilibration
Notes:     Use self-assembled quantum dots on metallic nanoparticle, excitons jump from QD to metal (Kamat ref. 127)
    Rather than band-bending in p-n, Fermi-level equilibration causes excited carriers to jump the gap
      Classify w/known redox pair
    Use redox agent to transfer charge to electrodes
Ecb = conduction ban E, nc = density of conduction electrons, Nc = charge carrier density

## Slide 11: Polymer-Semiconductor
Create junction between QD and organic polymer
  Lower efficiencies, but potentially much cheaper to mass produce
  Potential uses in medical devices
Use of
(Huynh 2002)
Notes: Image is just an example of a polymer that is used to exchange carriers with excited CdSe quantum dot
Poly-3(hexylthiophene)

## Slide 12: Nanorod Detail
(Kamat 2008)
100nm
100nm
Notes: Hyperbranched nanocrystal solar cell with a) controlled morphology of templated approaches b) no defects c) hyperbranching spans thickness d) 3-D CdSe structure e) CdTe structure, scale bar is 100nM
Also mainly for the cool visual

## Slide 13: QDSSC
Coupling QDs to larger semiconductor particles to improve charge transfer efficiency
  TiO2 has a larger bandgap, lower recombination rate
  CdSe can absorb wider range of frequencies
(Kamat 2008)
Notes: Can couple quantum dots to larger semiconductor particles, e.g. CdSe dot with TiO2 particle
  Coupling to larger bandgap increases power conversion efficiency
  Band diagram: electron excited in CdSe and moves to lower energy state in TiO2 where larger bandgap prevents recombination

## Slide 14: CdSe – TiO2 Absorbance
Example absorption spectra of CdSe QDs coupled to TiO2 semiconductor particles
  Size dependence is maintained even in composite systems
  Can match absorption to solar spectrum
(Kamat 2008)

## Slide 15: Size Effect on Efficiency
ICPE = Incident Photon to Charge-carrier-generation Efficiency
Unknown why it’s higher for smaller dots
One cool theory: hot electrons injected
  Might reduce thermalization losses
(Kamat 2008)

## Slide 16: Current State of QD-PVs
Maximum efficiency: 10.6%
  Compare to 34% single junction max, 45% multi-junction
Successful IR sensitive QD-PV
  Efficiency above 4%
Initial promise and huge sample space -> high research potential
  PV companies face economic and geopolitcal hurdles, high risk/reward market
    Helped with better PV technology
Notes: Molecular Engineering building: labs positively rolling in dough. I find that very comforting given climate change political drama

## Slide 17: References
Uhl, A., “A Solar Cell From a Material Science Perspective”, Univ. of Washington, HONORS 396 A.
Charles Kittel (1995) Introduction to Solid State Physics, 7th ed. Wiley, ISBN 0-471-11181-3.
https://en.wikipedia.org/wiki/Valence_and_conduction_bands (for image)
Schulze et al., Energy Environ. Sci.,2015, 8,103 (for image)
K. W. Johnston, A. G. Pattantyus-Abraham, J. P. Clifford, S. H. Myrskog, D. D. MacNeil, L. Levina, and E. H. Sargent, "Schottky-quantum dot photovoltaics for efficient infrared power conversion," Applied Physics Letters, vol. 92, p. 151115, 2008.
J. P. Clifford, K. W. Johnston, L. Levina, E. H. Sargent , “Schottky barriers to colloidal quantum dot films,” Applied Physics Letters, vol. 91, pp. 253117, 2007.
Kamat, Prashant V. "Quantum Dot Solar Cells. Semiconductor Nanocrystals as Light Harvesters †." J. Phys. Chem. C The Journal of Physical Chemistry C 112.48 (2008): 18737-8753. Web. 8 Oct. 2016.
Riel, B. J. "An Introduction to Self-assembled Quantum Dots." American Journal of Physics 76.8 (2008): 750. Web. 8 Oct. 2016.
Guyot-Sionnest, Philippe. "Colloidal Quantum Dots." Comptes Rendus Physique 9.8 (2008): 777-87. Web.
Huynh, W.U. “Hybrid Nanorod-Polymer Solar Cells.” Science 295.5564 (2002) 2425-427. Web. 14 Nov. 2016