## Slide 1: Formulating Design Problems (from 9-step model of design process)
Step 1 - Recognizing the Need
Step 2 - Defining the Problem
  Goals
  Objectives
  Constraints

## Slide 2: Recognizing the Need
Describes a current situation that is unsatisfactory.
Should be written in a negative tone
Establishes improvement in current situation as the ultimate purpose of the project.

## Slide 3: Engaging the Client
Sandra: “Jane, we need you to design a stronger bumper for our new passenger car.”
Jane: “Why do we need a stronger bumper?”
Sandra: “Well, our current bumper gets easily damaged in low-speed collisions, such as those that occur in parking lots.”
Jane: “Well, a stronger bumper may be the way to go, but there may be better approaches. For example, what about a more flexible bumper that absorbs the impact but then returns to its original shape?”
Sandra: “I never thought of that. I guess I was jumping to conclusions. Let’s restate the need as “there is too much damage to bumpers in low-speed collisions.” That should give you more flexibility in exploring alternative design approaches.”
Notes: 18

## Slide 4: The Importance of People Skills
This image is not available yet
Fig. 2.1

## Slide 5: Recognizing the Need -Automobile Bumper Problem
There is too much damage to bumpers in low-speed collisions
Notes: 20

## Slide 6: Defining the Problem-Goal
Brief, general, and ideal response to the Need.
Answer the question "How are we going to address this Need?"
Is so ideal that it could never be achieved, or so general that we cannot determine when it is achieved.
Its selection establishes the general direction of the design effort.

## Slide 7: Goal for Automobile Bumper Problem
Design an improved automobile bumper

## Slide 8: Some Approaches Eliminated by Choice of Goal*
Design a radar-based collision avoidance system
Add bumper-high rubber strips to parking lot structures
Place concrete “curbs” in all parking stalls
Reduce automobile use
Redesign parking lot traffic patterns
Establish minimum speed in parking lots

## Slide 9: Goals and Their Associated Design Options
Fig. 2.2

## Slide 10: Scope of Goal Statement
Need Statement:
  child-proof pill bottles are too difficult for people with arthritis to open.
Several potential Goal Statements :
  design a child-proof pill bottle that is easier to open
  design a child-proof pill container that is easier to open
  design a child-proof pill system for dispensing pills
  design a child-proof system for dispensing medication

## Slide 11: Defining the Problem-Objectives
Quantifiable expectations of performance.
Establish operating environment
Indicators of progress toward achieving Goal.
Define the performance characteristics of the design that are of most interest to the client
Facilitate determination of which alternative designs best meets expectations.

## Slide 12: Two Different Operating Environments for an Automobile Bumper
Fig. 2.3
Notes: 21

## Slide 13: Objectives for Automobile Bumper Problem
Design an inexpensive front bumper so the car can withstand a 5 mph head-on collision with a fixed concrete wall without significantly damaging the bumper or other parts of the car, or making the car inoperative. In addition, at the end of the useful life of the bumper, it must be easily recyclable.

## Slide 14: Objectives Should be Measurable
This image is not yet available
Fig. 2.4

## Slide 15: Itemized List of Objectives
inexpensive
no significant damage to bumper
no significant damage to other parts
easily recyclable
operative

## Slide 16: Operating Environments for Objectives
Pre-Collision: 5mph head-on into a fixed concrete wall
Post-Collision: 15 mph

## Slide 17: Damage to Vehicle in Bumper Test
This image is not yet available
Fig. 2.5

## Slide 18: Revised Need Statement
There is too much damage to cars in low-speed collisions

## Slide 19: Revised Goal for Automobile Bumper Problem
Design an improved front bumper

## Slide 20: Basis for, and Units of, Measuring Objectives
Objective | Measurement Basis | Units
Inexpensive | Unit manufacturing cost for a production run of 50,000 | dollars
No significant damage to bumper | Distance bumper is pushed into body | inches
No significant damage to other parts | Repair cost | dollars
Easily recyclable | Amount of aluminum | lb
Retain maneuverability | Turning radius | ft
Retain braking capability | Braking distance | ft
Table 2.1
Notes: Note that the previous objective that the car be operative after a collision has been split into two objectives dealing with maneuverability and braking.

## Slide 21: Defining the Problem-Constraints
Constraints establish permissible range of the design and performance parameters
yes/no constraints (must use 3/8”-24 UNF SAE grade 5 bolts)
equality constraints (must be 18” high)
inequality constraints (cannot weigh more than 50 lb, must hold at least 50 lbs of steam, must be between 12” and 15” long)

## Slide 22: Constraints for Automobile Bumper Problem
In order to prevent over-riding bumpers in collisions between automobiles, the bumpers should be installed 18” up from the ground.
The weight of the bumper cannot exceed 50 lb.
The mounting brackets on the bumper must be between 8.0” and 12.5” from the center so they match with the brackets attached to the automobile frame.

## Slide 23: Complete (Revised) Problem Statement for Automobile Bumper Project
Goal
  Design an improved front bumper
Objectives (with operating environments, basis for measurement, and units)
  Inexpensive
  No significant damaging to bumper
  No significant damaging to other parts
  Easily recyclable
  Retain maneuverability
  Retain braking capability
Constraints
  Should be installed 18” up from the ground.
  Weight of the bumper cannot exceed 50 lb.
  Mounting brackets must be between 8.0” and 12.5” from the center
  Lights must work after collision
  Radiator must not leak after collision
  Doors must work after collision

## Slide 24: Trade-offs Between Objectives and Constraints
Restating the problem in a slightly different way can result in some objectives becoming constraints and vice-versa.
the objective “not causing significant damage” can be reworded as a constraint “not costing more than $200 to repair”.
It may be desirable to include both in the problem statement.

## Slide 25: Unambiguous Objectives
All objectives must be unambiguous
Use longer definitions if necessary to remove ambiguity
Objectives should be fully documented
All objectives should have units
Spend at least twice as much time on developing objectives than you would like to

## Slide 26: Transforming Objectives into Criteria
Objectives
  Quantifiable expectations of performance
Criteria
  Value-free compact descriptors of performance associated with objectives

## Slide 27: Objectives and Criteria for Automobile Bumper
Objective | Units | Criteria
Inexpensive | dollars | cost
No significant damage to bumper | inches | Amount of damage to bumper
No significant damage to other parts Easily recyclable | dollars lb | Amount of damage to other parts Recyclability
Retain maneuverability | ft | Maneuverability
Retain braking capability | ft | Braking capability
Table 2.2

## Slide 28: Criteria Tree for Automobile Bumper
This image is not yet available
Fig. 2.6

## Slide 29: Developing Design Criteria for Power Transmission Between Parallel Shafts
Identify Classes of Options (e.g., Belts, Chains, and Gears)
List Advantages/Disadvantages of Options
Develop Consolidated List of Criteria.
  1. Shock Protection
  2. Noise
  3. Large separation distance
  4. High speed capability
  5. Lubrication requirement
  6. Misalignment
  7. Separation distance flexibility
  8. Installation/replacement ease
  9. Bearing loads
  10. Slippage/creep
  11. Size
  12. Life expectancy
  13. Operating temperature
  14. Speed flexibility
  15. High torque capability

## Slide 30: Ambiguity of Life Expectancy Criterion
total life or operating life (e.g., corrosion during long idle periods) ?
operating conditions for determining life expectancy (e.g., time in transit for portable equipment)?

## Slide 31: Criteria Tree for Power Transmission Between Parallel Shafts
Fig. 2.7
Notes: 29

## Slide 32: Design Criteria for an Automobile Horn*
1. Ease of achieving 105-125 DbA
2. Ease of achieving 2000-5000 Hz
3. Resistance to corrosion, erosion, and water
4. Resistance to vibration, shock, and acceleration
5. Resistance to temperature
6. Response time
7. Complexity: number of stages
8. Power consumption
9. Ease of maintenance
10. Weight
11. Size
12. Number of parts
13. Life in service
14. Manufacturing cost
15. Ease of installation
16. Shelf life
Notes: This is Exercise 13 at the end of Chapter 2.

## Slide 33: Criteria Tree for Automobile Horn*
Three of the original 16 criteria (service life, manufacturing cost, ease of installation) may duplicate (at least partially) several others. Can redefine criteria to eliminate overlap.

## Slide 34: Functional Analysis
Fig. 2.9
Fig. 2.8

## Slide 35: Functional Analysis System Diagrams for Conventional and Cogeneration Power Plants
Fig. 2.10
Notes: 24

## Slide 36: Subfunction Diagram for a Steam Turbine Power Plant
Fig. 2.11
Notes: 25

## Slide 37: Subfunction Diagram for Steam Generation (Function 1)
Fig. 2.12

## Slide 38: Functional Analysis Diagram for a Tea Brewing Machine*
Shown below is one of many possibilities.
Focus is on the functions, rather than on the components that perform those functions.

## Slide 39: Functional Analysis Diagram for a Clothes Dryer
This image is not yet available
Fig. E2.5.1

## Slide 40: Structure of Quality Function Deployment Chart
Fig. 2.13
Notes: 26

## Slide 41: QFD Chart for Automobile Bumper
This image is not yet available
Fig. 2.14
Notes: 27

## Slide 42: House of Quality for Automobile Bumper
This image is not yet available
Fig. 2.15
Notes: 28

## Slide 43: QFD Chart for a Shopping Cart*
Notes: This is Exercise 10 at the end of Chapter 2.

## Slide 44: Problem Formulation Terminology
Need
Goal
Objectives
Constraints
Criteria
Attributes
Characteristics
Functions
Specifications
Performance Specifications
Design Specifications
Customer Requirements
Engineering Requirements
Design Parameters
Performance Parameters
Notes: 23