TCS 372A                 Solution                  Homework Set #7 - Chapter 11: 4, 5, 13, 16                    Due 11/15/06

All problems completed

  - Given a 16-bit processor  and the following instruction:

| 200 | Load to AC | Mode |
| --- | --- | --- |
| 201 | 500 |  |
| 202 | Next Instruction |

Source register is R1 which contains 400

Base register contains 100

Location 399 contains 999, Location 400 contains 1000, etc

a) Direct:  Effective Address = 500 (value in location 201)

Operand = 1000+100 = 1100

b) Immediate: Effective Address =  201 (location 201)

Operand = 500

c) Indirect: Effective Address = 1100 (value in location 500 = 1100)

Operand = 1700

d) PC relative: Effective Address = 202 + 500 = 702 ((PC) + 500)

Operand = 1302

e) Displacement: Effective Address =  (R1) + 500 = 900

Operand = 1500

f) Register: Effective Address = (R1)

Operand = 400

g) Register indirect: Effective Address = ((R1)) = 1000

Operand = 1700

h) Autoindexing with increment, using R1: Effective Address =  (R1) = 400 (assume post indexing)

Operand = 1000

  - A PC relative mode branch instruction at memory location 256028 base 10 is 3 bytes long, and the signed displacement is -31 base 10.

The next instruction is at 256031 and the branch is -31, so the next address is 256031-31= 256000

  - Given the following instruction on a stack machine, the stack contains:

Instructions:			Stack:

PUSH 4			4

PUSH 7			7	4

PUSH 8			8	7	4

ADD				15	4

PUSH 10			10	15	4

SUB				5	4

MUL				20

  - The op code formats are:

2 operand instructions have 16- 6 – 6 = 4 bits for op codes

1 operand instructions have 16-6 = 10 bits for op codes

0 operand instructions have 16 bits for op codes

At least one bit must be used for specifying that it is a 1operand instruction.  That leaves 9 bits for the op code.  So, there can be 29 = 512 op codes.