TCSS 465A

Embedded Real-Time System Programming

Midterm - Spring 2006

1) CLEARLY show on a timing diagram the parameters for a real time periodic task:

- Compute time Ci

- Finish time f i

- Arrival time a i

- Phase  i

- Start time s i

And define:

- Response time:

R i  =  f i  -  a i

- Lateness:

L i  =  f i  -  d i

- Laxity:

R i  =  d i  - a i -  C i

- Name five properties that real-time systems must have to support critical applications:

1.  Timeliness – must meet deadlines appropriately

2.  Design for peak-load – Can’t crash under peak loads

3.  Predictability – Must not have unanticipated surprises

4.  Fault Tolerance – The system must be robust and fail-safe

5.  Maintainability – Must be modifiable as requirements evolve

- Define and distinguish between each of the following scheduling algorithms:

  - Earliest Due Date

1 |  sync | Lmax   : Independent, sync, aperiodic, non-preemptive tasks.  Minimize Lmax

Tasks are scheduled in order of non-decreasing deadlines.  Provides optimal schedule

  - Earliest Deadline First

1 |  preem | Lmax : Independent, preemptive, dynamic tasks.   Minimize Lmax

Task with earliest deadline has priority.   Provides optimal schedule.

  - Latest Deadline First

1 |  sync, prec | Lmax : Precedence, sync, aperiodic, non-preemptive tasks.  Minimize Lmax

Schedule backwards with latest deadline task scheduled “first”.  Provides optimal schedule.

- Apply EDF to schedule the following set of tasks Ji with precedence constraints:

Apply LDF to schedule the set of tasks:

5)   Verify the schedulability according to the Rate Monotonic algorithm for the following set of periodic tasks.

Construct the schedule using RM.

- You did two projects using the NetBurner A/D converter.  In the first you used Port A as a 4 bit output port.  What did you need to do to program it?

Initialize: The default on the Configuration and Control registers are for digital I/O on Port A,

so nothing was required.  The Port A Data Direction Register bits needed to be

programmed for output.

Output: The output follows writes to the buffered Data Register in the A/D.

On the second project you used both Port A and Port B as A/D input Ports.  What did you need to do to program it in that mode?

Initialize: The Configuration Register needs to be set to “stop”, Port A & B Control Registers set,

Port A & B Data Direction Registers set, Port A & B QADC timing registers set, and

the Configuration Register set to “start”.  The Queue must be programmed for the

sampling sequence, and finally, the scan initiated.

Input:  The input is obtained by reading from the queue.

- On the third project, what did your thermistor characteristic look like (resistance vs temperature) ?

What should the voltage vs temperature curve look like in the circuit?

See graph above.