TCSS 371A

Computer Organization

Fall 2009

Final Exam

December 17, 2009

Solution

Name ______________________________

Clearly show ONLY the work and answers you want graded!

Please contain your submission to the space provided.

Use scratch paper for preliminary work.

1)  a) Add -41 to 19 using 8 bit 2’s complement arithmetic.

-41 = - 00101001  = 11010111

19                         = 00010011

11101010 =  - 00010101 = -22

b) Show the largest number that can be stored in a 4 bit, 2’s complement register?

Largest = 0111 = 7

Show the smallest?

Smallest = 1000 = - 1000 = -8

- Find the IEEE Floating point representation of - 1.5   Show your work!

{s e e e e e e e e f f f f f f f f f f f f f f f f f f f f f f f }  Hint: exponent is excess 127

-1.5 ( sign=1,  exponent=0 which in exec 127 is 01111111, fraction=1000000000---00

-1.5 = 1 01111111 10000000000000000000000

d) Show using a truth table that NOT(A OR B) = (NOT A) AND (NOT B)

A   B  |    (A OR B)   NOT(A OR B)    NOT A     NOT B    (NOT A) AND (NOT B)

0   0   |         0                     1                   1              1                          1

0   1   |         1                     0                   1              0                          0

1   0   |         1                     0                   0              1                          0

0   1   |         1                     0                   0              0                          0

The columns   NOT(A OR B)   and   (NOT A) AND (NOT B)   are identical

e) Given a machine language Branch instruction with a 5 bit offset (2’s complement), find the highest resultant PC address.  (assume the instruction is located at location x4000)

Highest = [PC] + 15 = x4001 + xF = x4010

Find the lowest.

Lowest = [PC] -16 = x4001 – x10 = x3FF1

2) a)  What is the word size of  our LC-3 machine?

16 bits

What is the number of words in the memory space of the LC-3 machine?

216  = 64K

How many 1Kx4 memory chips would it take to fill the memory space of the LC-3?

4 would give as 1K x16 or 1K words

4 x 64 = 256  would give us the 64K x 16 space

b)  What is overflow in a computer computation?

A result that is too large to fit in the machine word

e.g. adding two positive numbers and getting an apparent negative result

or adding two negative numbers and getting an apparent negative result

- Define an algorithm

1)  Definiteness - precise

2)  Effective Computability – each step can be done on a computer

3)  Finiteness – can be done in a finite number of steps

- What are the major states of a computer instruction cycle?

1)  FETCH Instruction

2)  DECODE Instruction

3)  EVALUATE Operand Addresses

4)  READ Operands

5)  EXECUTE Operation

6)  STORE Results

3) a)  Show a memory map for the LC-3 include op sys, vectors, device registers, user program, stack,

PC, Stack Pointer, Global Pointer, and Frame Pointer.

b) Name the five addressing modes of the LC-3, and explain where the operand is for each:

1. register – the operand is in one of the 8 general purpose registers

2. immediate – the operand is in the instruction (limited to -16 to +15)

3. pc relative – the operand is in memory location [PC] + the offset specified in the instruction

4. base relative – the operand is in memory location [base reg] + the offset spec in the instr

5. indirect – the PC relative memory address is a pointer to the memory address of the operand

c) Convert the following assembly language to machine code (show it in binary and hex):

.org   	x3000

DATA:   	.FILL 	x2400				0010  0100  0000 0000	2400

LD     	R1,  DATA			0010  001  111111110	23FE

ADD  	R1,  R1,  # -5			0001  001  001  1  11011	127B

LOOP:  	BR nzp  LOOP			0000  111  111111111	0FFF

.END

4. Develop a clear well commented assembly language program that reads and echoes an endless string of characters from the keyboard using your interrupt routine.  Your program should assume the interrupt routine uses your user stack (you will recall that the simulator erroneously doesn’t use the supervisor stack).  KBSR = xFE00,  KBDR=xFE02,  KBIV= x0180.

Please develop your program on scrap paper and only enter the code you want me to grade.  Thanks!

- Main program:

Initialize the Stack to xFE00:

.ORIG  x3000

BEGIN       	LD    R6, STK_PTR  	   ; initialize stack pointer to xFE00

;   builds downward

Load the interrupt vector:

LEA	   R0, ISR     	   ; load keyboard interrupt vector: x80

STI	   R0, KBIV        ;   (location 180)

Enable the Keyboard:

LD	   R0, KBSRIE   ; enable keyboard interrupts

STI	   R0, KBSR

Loop forever:

LOOP	BRNZP  LOOP              ; loop forever !

HALT

- Write an Interrupt Service program which gets the character inputted and echos it with a Trap instruction.  Save R0 on the stack during the interrupt service routine

ISR	    	ADD	   R6, R6, #-1      ; push R0, because we'll use it

STR	   R0, R6, #0

LDI	   R0, KBDR       ; reset interrupt (by reading KBDR)

OUT			    ; echo the input character

LDR	   R0, R6, #0   	    ; pop R0

ADD	   R6, R6, #1

RTI			    ; return from the interrupt

- Define your Data / References here:

STK_PTR      .FILL    xFE00          ; initial stack address

KBSR	  .FILL    xFE00          ; keyboard status register

KBSRIE      	 .FILL     x4000         	;    bit 14 is interrupt enable bit

KBDR	 .FILL     xFE02        	; keyboard data register

KBIV	   	 .FILL     x180           	; keyboard interrupt vector

.END

5. a ) Show the format of a frame or  activation record that begins with frame pointer:

Caller’s Frame Pointer (R5)

Caller’s Return PC (R7)

Function Return Value

Function Pass Values

R5(    Local Variables

For the C program, identify the contents of the stack just before the return from the function:

#include <stdio.h>

void Func(int *p);

int main()

{

int valueA = 3;

int valueB = 4;

valueB = Func(&valueA);

}

void Func(int *x)

{

int a=2;

*x = 1;

}

xEFF3

xEFF4

xEFF5   Func local variable a = 2	              <- FramePtr (Func)

xEFF6   R5 (Frame Ptr for main)

xEFF7   R7 (PC stored to return to main)

xEFF8   return value space

xEFF9   pass value = *valueA = xEFF9

xEFFA  main local variable valueB = 4

xEFFB  main local variable valueA = 1	     <- FramePtr (main)

xEFFC  R5 (FramePtr)

xEFFD  R7 (PC stored)

xEFFE  return value space

xEFFF		      	                            <- StkPtr, FramePtr (initially)