## Slide 1: Towards a Biarticular Prosthesis:
Model Development and Sensitivity Analysis of Clutched Spring Parameters
Andrea Willson
University of Washington
VA Center of Excellence for
Limb Loss Prevention &
Prosthetic Engineering

## Slide 2: Introduction
Gastronemius (GAS): accelerates leg into swing in late stance phase [1]
Soleus (SOL): accelerates trunk forward [1]
Other muscles compensate for lack of biarticular GAS function [2]
Neptune RR, et al. J Biomech, 34, 1387-1398, 2001.
Zmitrewicz RJ, et al. J Biomech, 40, 1824-1831, 2007.
Gastrocnemius
Soleus
GAS
SOL
Notes: Passive prostheses only match uniarticular function of the soleus

## Slide 3: Overall Research Goals
Develop biarticular clutched spring prosthesis that replicates functional role of GAS
  Reduce compensatory muscle forces
  Reduce metabolic cost of amputee walking
Use simulation to determine optimal spring parameters

## Slide 4: Specific Aims
Develop amputee model for OpenSim
Analyze how variations in spring parameters affect knee and ankle dynamics
  Attachment point
  Clutch timing
  Stiffness

## Slide 5: Amputee Model
Residual limb mass properties derived from literature [4,5]
CAD model based on prosthesis measurements used to determine prosthetic mass properties
Pin joint created in same relative position as intact ankle to replicate flexion in prosthesis
4. Silverman AK, Neptune RR. J Biomech, 45, 2271-2278, 2012.
5. Smith JD, et al. J Vis Exp, 87, 2014.

## Slide 6: Methods
Use Static Optimization with amputee model and passive biarticular spring element
Clutch engaged
Choose baseline spring parameter values based on physiological GAS
  Proximal Attachment point
  Clutch timing
  Stiffness
Vary each parameter individually to assess changes in:
  Biarticular spring force
  Biarticular spring contribution to knee, ankle moment

## Slide 7: Baseline Trial
Spring matched to physiological GAS parameters:
Stiffness of 100 N/mm [6]
Clutch timing = GAS length @20% gait cycle
Proximal and Distal attachment points match GAS
6. Krishnaswamy P, et al. PLoS Comput Biol, 7 (3), 2011.

## Slide 8: Results: Varied Proximal Attachment Point
Notes: RL and stiffness are both directly related to force production, while MR can alter the joint moment contribution without requiring an increase in force.

## Slide 9: Results: Varied Clutch Timing

## Slide 10: Results: Varied Spring Stiffness

## Slide 11: Discussion
Knee moment arm
Knee moment Ankle moment
Knee moment Ankle Moment
Clutch engagement time
Knee moment Ankle Moment
Spring stiffness

## Slide 12: Implications for Device Design
Joint moment contributions are very sensitive to changes in attachment point
  Larger moment arm at knee will allow for the spring stiffness to be greatly reduced
  Soft tissue compliance at proximal attachment

## Slide 13
Contributors:
Routson, Rebecca 1,3
Steele, Kat 1
Czerniecki, Joseph 2,3
Morgenroth, David 2,3
Aubin, Patrick 1,3
1. University of Washington
Department of Mechanical Engineering
2. University of Washington
Department of Rehabilitation Medicine
3. Department of Veterans Affairs
RR&D Center of Excellence, Seattle, WA USA
Acknowledgments