University of Washington, Bothell  		&  	Cascadia Community College

North Creek Stream Channel &

Floodplain Wetlands

This 58-acre restoration has reestablished a natural stream channel, reconnected the stream to its floodplain, and is creating a native floodplain ecosystem. The site provides a rich educational resource for this campus and the surrounding community.

##### Project & Site Synopsis

# Land Use History

Before European settlement, the campus lowlands consisted of a complex array of stream channels, backwater lakes, and depressions that were part of the junction environment where North Creek flowed into "Squawk Slough" (now the Sammamish River). The floodplain would have been primarily forested with some scrub-shrub and emergent communities. Dominant tree species would have been Western red cedar, Black cottonwood, Douglas-fir, Big leaf maple, and Red alder.

By 1895, the site had been logged and by 1916 large portions of the North Creek channel system, including that on campus, had been straightened and confined within levees. North Creek served as a flume for delivery of logs from the watershed to Lake Washington sawmills. Following logging and since about the 1930's, the site had been used for grazing or farming. Extensive drainage systems were constructed to manage groundwater and surface waters.

Off site changes have permanently altered hydrological conditions. Construction of the Lake Washington ship canal and locks in 1913 - 1916 lowered the lake level by about 12 feet, steepening the lower reaches of North Creek. Rapid urbanization in the watershed over the last 60 years has increased impervious surfaces and consequently altered the stream flow characteristics of North Creek.

# Original Site Conditions

Prior to restoration, the North Creek channel was straight, channelized, and confined within artificial levees. The creek had limited opportunity to connect with its floodplain and when it did flood drainage through ditches was rapid. This resulted in a lack of contact time of floodwaters with the floodplain with direct consequences for water quality and other resources for anadromous and resident fish in the North Creek ecosystem. In addition, a host of non-native herbaceous weeds (i.e., reed canary grass) dominated the site. Along the levees, a mosaic of sparse native and non-native shrub and herbaceous plant communities existed.

# A Mandate for Restoration

Campus development required filling of approximately 6 acres of hillslope wetlands. Mitigation for this wetland destruction was legally mandated. While it was possible to meet the mitigation requirements on the site without restoring the entire floodplain and channel, the State of Washington made a commitment to environmental enhancement of the site that went beyond that which was strictly necessary from a regulatory standpoint. The State decided to restore the structure and functioning of the entire North Creek riverine ecosystem on the site. The proposed restoration was granted final approval in June of 1998 by regulatory agencies.

# Project Overview

This project is one of the largest floodplain restorations in the Pacific Northwest. It is unique in the emphasis on the restoration of underlying physical, chemical and hydrological features of the stream channel and floodplain as well as the biological communities. The project design and initial implementation was led by L.C. Lee & Associates in coordination with the M. A. Mortenson Company, the general contractor for campus construction. Subsequent monitoring and maintenance has been accomplished by the campus Facilities Services unit in coordination with Blasland, Bouck & Lee, Inc. and most recently Arcadis, Inc.

# The Stream Channel

The new channel is designed to reflect a natural junction environment channel form and is constructed to allow flooding at least annually. The new main channel was designed with bed and bank features, meanders, and a variety of in-channel habitats, including pools, riffles, and large wood. A secondary channel was designed to engage at higher (flood-stage) flow volumes.

# The Floodplain

The floodplain is characterized by a mosaic of native forested and scrub-shrub communities, planted after aggressive measures to control non-native species were implemented. Topographic variation and large woody debris, so common in our regional floodplains, were purposely added. The establishment of fundamental hydrology and topography along with effective monitoring and adaptive management should allow the natural successional development of this floodplain ecosystem.

##### Project Context: the North Creek Watershed

The 127-acre co-located campus of University of Washington-Bothell and Cascadia Community College is located along North Creek, just upstream from its junction with the Sammamish River near the north end of Lake Washington (Figure 1).  This location places the UWB – CCC wetlands at the distal (bottom) end of the North Creek Watershed that runs through southern Snohomish County and northern King County.

The 32-square-mile North Creek watershed (Fig. 2) is a part of the Sammamish watershed, which itself is located within the management and planning district called the Water Resource Inventory Area # 8 (WRIA 8 – the Sammamish, Cedar and Lake Washington Watersheds). The headwaters of North Creek are located in south Everett and extend about 12.5 miles through largely residential and commercial areas down to its junction with the Sammamish River next to the UW Bothell campus. Despite the development pressures, significant natural elements remain along the stream (note green / shaded areas along the stream on the map).

The watershed was formed about 12 - 14,000 years ago with the retreat of the last major continental glaciation. Subglacial streams cut a series of north – south valleys through which Swamp, North and Little Bear creeks presently run. The soils were primarily formed from the glacial till and outwash material deposited during that glacial recession. Most of these soils (Alderwood and Everett series) are very coarse and poor in nutrients and water holding capacity. However, alluvial and muck soils have built up over years in some valley-bottom depressional wetland locations. These muck soils are very deep, poorly drained and contain deep deposits of peat, some of which have been mined.

Urbanization has been the dominant impact over the last few decades. In fact, the North Creek watershed is one of the most rapidly urbanizing areas in the Puget Sound region, with estimates of impervious surface area rising rapidly and exceeding 40% in the late 1990s. North Creek once supported healthy populations of different salmon species (e.g., Chinook, sockeye, coho, and sea run cutthroat trout), but only highly reduced populations of sockeye and chinook salmon remain.

North Creek itself is a low gradient stream, changing only about 100 feet in elevation over more than 12 miles. Water quality monitoring has revealed considerable areas of concern, with elevated levels of phosphorus, fecal coliform bacteria and high turbidity (suspended sediment). Many of the water quality problems stem from non-point sources, such as vehicles, pets, agriculture, and residential activities.

North Creek flows through 5 jurisdictions, the city of Everett, the city of Mill Creek, Snohomish County, King County, and the city of Bothell. Each jurisdiction has unqiue development strategies, regulations and protections, creating a challenging situation for coherently managing this stream ecosystem.

##### Recent History of the Site

Before European settlement, the campus lowlands consisted of a complex array of stream channels, backwater lakes, and depressions that were part of the junction environment where North Creek flowed into "Squawk Slough" (now the Sammamish River). The floodplain would have been primarily forested wetland with some scrub-shrub and emergent communities. Dominant tree species would have included Thuja plicata (Western red cedar), Populus trichocarpa (Black cottonwood), Psuedotsuga menziesii (Douglas-fir), Acer macrophyllum (Big leaf maple), and Alnus rubra (Red alder). Layers of diatomaceous earth imbedded in floodplain soils suggest this site experienced considerable periods of inundation as part of the wet slough system between Lake Sammamish and Lake Washington.  Further evidence of such persistent wetland communities is provided by the 1871 Territory of Washington Land Survey (Figure 3).

By 1895, the site had been logged and by 1916 large portions of the North Creek channel system, including that on campus, had been straightened and confined within levees. This was done so that North Creek could serve as a flume for delivery of logs from the watershed to sawmills located on the shore of Lake Washington. At that same time, important off site changes permanently altered the hydrological conditions of the site. Construction of the Lake Washington ship canal and locks from 1913 to 1916 lowered the lake level by about 12 feet, causing the lower reaches of North Creek and the Sammamish River to cut down and steepen. The site remained a wetland but was drier, no longer characterized by extensive standing water. Thus, the opportunity arose to use the land for pasture and crops. Since about the 1930s, the site had been used for cattle grazing and farming. Extensive drainage systems (e.g., ditches and tile drains) and dikes were constructed to manage groundwater and surface waters. Pastures were planted with fast growing plants tolerant of wetland conditions, most notably, the invasive European grass, Reed canary grass (Phalaris arundinacea). Along the levees, a mosaic of sparse native and non-native shrub and herbaceous plant communities existed. The creek had limited opportunity to connect with its floodplain and when it did flood drainage through ditches was rapid. This resulted in a lack of contact time of floodwaters with the floodplain with direct consequences for water quality and other resources for wildlife such as anadromous and resident fish in the North Creek ecosystem (Figure 4).

Rapid urbanization in the watershed over the last 60 years has increased impervious surfaces and consequently altered the stream chemistry and flow characteristics of North Creek (e.g., increased flood frequency and intensity).

Restoration

We are extremely fortunate to have a living wetland laboratory right on our campus at UWB and CCC – in the form of the largest floodplain wetland restoration in our region. The campus was initially constructed on this site from 1998 to 2000. Although the campus buildings were placed on the hillslope above the floodplain of North Creek, their construction required the filling of approximately six acres of hillslope wetlands (Figure 5).

Federal, state and city of Bothell regulations required mitigation for these construction activities. The state proposed to restore the entire 58-acre floodplain wetland portion of the site to mitigate for construction impacts on the hillside wetlands. This was accepted by the federal, state, and local regulatory agencies and the construction permits were issued requiring the complete restoration of the floodplain wetlands along with 10 years of monitoring (compliance monitoring) to ensure compliance with the intention of the permits.

The overall project design is unique in its emphasis on the restoration of physical, chemical and hydrological features and processes that underlie a healthy stream and floodplain ecosystem. A new, meandering stream channel and complex floodplain microtopography were created as a template for this effort.

Floodplain wetlands exist by virtue of the hydrological connection between the stream and the floodplain provided by regular floods. Flooding facilitates geochemical exchange between aquatic and terrestrial components of the ecosystem and creates a dynamic ecological system through regular disturbance. Thus, one of the first foci of project design was to reconnect North Creek with its surrounding floodplain. It was decided that natural stream channel morphology would be returned to North Creek by constructing a new channel system that reflected the morphological and hydrological characteristics found at reference sites in the Puget Sound Lowlands. The new stream channel system would be constructed to allow flood over its banks approximately once a year, relinking the channel and floodplain components of the North Creek ecosystem on site. The new main channel was designed with bed and bank features, meanders, and a variety of in-channel habitats, including pools, riffles, and large wood. A secondary channels was designed to engage at different flow volumes and provide backwater habitat at lower flow levels (Figure 6).

The channel was engineered based upon data from channel form of comparable less-impacted streams in the Puget Sound area. This included the incorporation of woody debris elements, both along the stream bank (e.g., bank deflection log jams) and at the juncture of the primary and secondary channels (a bar apex log jam) (Figure 7). The bank deflection log jams were placed carefully to constrain (but not prevent) the degree of future channel movement, so as to not jeopardize campus buildings and highway overpass structures.

Beside the stream channels, a tremendous effort went into the initial creation of overall site topography. Levees were removed and flattened pastures were converted into a floodplain that slopes very gradually alongside the descending stream. During this process, the southern half of the site was scraped to a depth of 12 inches and much of the northern half was buried under more than 24 inches of fill. These processes helped to remove and initially suppress reed canary grass and other invasives. Because the site is so large, planting took place in phases from the fall of 1998 to the spring of 2002 (Figure 8).

The planted floodplain is characterized by a mosaic of 20 native forested, scrub-shrub, and emergent wetland communities (Table 1). The majority of the site was planted to forested wetland communities. Within all of the communities, small-scale topographic variation (“microdepressions” with central depressions called “pits” and surrounding raised areas termed “mounds”) and large woody debris, so common in our regional floodplains, were purposely added. The site was planted in 261 distinct planting polygons, based upon the expected environmental conditions (e.g., topography, hydrology) (Figure 9). The establishment of fundamental hydrology and topography along with effective monitoring and adaptive management should allow the natural successional development of this floodplain ecosystem (Figures 10 and 11).

I. Evergreen Forest Types

Douglas-fir (Psuedotsuga menziesii)

Big leaf maple (Acer macrophyllum)

Red alder (Alnus rubra)

Western hemlock (Tsuga heterophylla)

Red elderberry (Sambucus racemosa)

Red-flowering currant (Ribes sanguineum)

Thimbleberry (Rubus parviflorus)

Baldhip rose (Rosa gymnocarpa)

Vine maple (Acer circinatum)

Salal (Gaultheria shallon)

Serviceberry (Amelanchier alnifolia)

Hawthorn (Crataegus douglasii)

Bitter cherry (Prunus emarginata)

Sitka brome (Bromus sitchensis)

Timber oatgrass (Danthonia intermedia)

Shooting star (Dodecatheon hendersonii)

II. Floodplain & Riparian Forest Types

Red alder (Alnus rubra)

Wetsern red cedar (Thuja plicata)

Black cottonwood (Populus trichocarpa)

Big leaf maple (Acer macrophyllum)

Oregon ash (Fraxinus latifolia)

Sitka spruce (Picea sitchensis)

Pacific crab apple (Malus fusca)

Bog birch (Betula glandulosa) *

Viburnum (Viburnum edule)

Pacific willow (Salix lasiandra)

Scouler willow (Salix scouleriana)

Salmonberry (Rubus spectabilis)

Snowberry (Symphorocarpus albus)

Cascara (Rhamnus purshiana)

Vine maple (Acer circinatum)

Indian plum (Oemlaria cerasiformis)

Twinberry (Lonicera involucrata)

Labrador-tea (Ledum groenlandicum) *

Bog laurel (Kalmia polifolia) *

Ninebark (Physocarpus capitatus)

Skunk cabbage (Lysichitum americanum)

Lady fern (Athyrium felix-femina)

Piggy back (Tolmeia menziesii)

Slough sedge (Carex obnupta)

Dewey sedge (Carex deweyana)

Fox sedge (Carex vulpioidea)

Beaked sedge (Carex rostrata)

Beakrush (Rhychospora alba) *

Water parsley (Oenanthe sarmentosa)

Lily-of-the-valley (Maianthemum dilatatum)

# III. Floodplain Scrub-Shrub Types

Pacific willow (Salix lasiandra)

Sitka willow (Salix sitchensis)

Redosier dogwood (Cornus stolonifera)

Hardhack spirea (Spirea douglasii)

Small-fruited bulrush (Scirpus microcarpus)

Tapertip rush (Juncus acuminatus)

Slough sedge (Carex obnupta)

IV. Emergent Marsh Types

Lenticular sedge (Carex kelloggii)

Sawbeak sedge (Carex stipata)

Slough sedge (Carex obnupta)

Water parsley (Oenanthe sarmentosa)

Water sedge (Carex sitchensis / C. aquatilis)

Marsh cinquefoil (Potentilla palustris)

Buckbean (Menyanthes trifoliata)

V. Microdepressions

Mound:

Oregon ash (Fraxinus latifolia)

Western red cedar (Thuja plicata)

Douglas-fir (Psuedotsuga menziesii)

Paper birch (Betula papifera)

Western hemlock (Tsuga heterophylla)

Red huckleberry (Vaccinium parvifolium)

Salal (Gaultheria shallon)

Pit:

Hardhack spirea (Spirea douglasii)

Bog birch (Betula glandulosa)

Sitka sedge (Carex sitchensis)

# Slough sedge (Carex obnupta)

Monitoring and Maintenance

Since the initial phases of the restoration project, the abundance and diversity of animal species have been increasing. Some taxa are being formally monitored, while others are only under casual observation at this time. Table 2 lists some representative species that have been observed (not including insects), along with some that are known to have historically been present in the lower reaches of the North Creek watershed. This is not a comprehensive list.

Mammals

Mule / Black-tailed deer		Odocolieus hemionus

Coyote				Canis latrans

River otter			Lutra canadensis

Racoon				Procyon lotor

Beaver				Castor canadensis

Mouse				Mus musculus

Deer mouse			Peromyscus maniculatis

Pacific mole			Scapus orarius

Reptiles & Amphibians

Pacific treefrog			Hyla (Pseudoacris) regilla

Red-legged frog			Rana aurora

Bullfrog			Rana catesbeiana

Common garter snake		Thamnophis sirtalis

Northwestern garter snake	Thamnophis ordinoides

Birds

Great blue heron	Ardea herodias

Canada goose		Branta canadensis

Mallard duck		Anas platyrhynchos

Osprey			Pandion haliaetus

Red-tailed hawk	Buteo jamaicensis

American crow		Corvus brachyrhynchos

American robin		Turdus migratorius

Black-capped chickadee	Parus atricapillus

European starling	Sturnus vulgaris

Spotted sandpiper	Actitis macularia

Belted kingfisher	Megaceryle alcyon

Downey woodpecker	Dendrocopos pubescens

Willow flycatcher	Empidonax traillii

Marsh wren		Telmatodytes palustris

Common yellowthroat	Geothlypis trichas

Red-winged blackbird	Agelaius phoeniceus

House finch		Carpodacus mexicanus

Savannah sparrow	Passerculus sandwichensis

House sparrow		Passer domesticus

Killdeer		Charadrius vociferous

Fish

Chinook salmon	Oncorhynchus tschwytscha

Coho salmon		Oncorhynchus kisutch

Sockeye & kokanee	Oncorhynchus nerka

Steelhead rnbw trout*	Oncorhynchus mykiss

Cutthroat trout*		Oncorhynchus clarki

3-spine stickleback*	Gasterosteus aculeatus

Sculpin	*		Cottus spp.

Speckled dace*		Rhinichthys osculus

Redside shiner*		Richardsonius balteatus

Large-scale sucker *	Catostomus macrocheilus

Yellow perch*		Perca flavescens

Largemouth bass*	Micropterus salmoides

Smallmouth bass*	Micropterus dolomieui

Shiners	*		Notropis spp.

Compliance monitoring based upon the construction permits (Army Corp of Engineers; WA State dept. of Ecology; City of Bothell) is required for ten years following the date of project “completion”. The official project completion date was in the late spring of 2002. The compliance monitoring schedule is:

A variety of parameter are monitored to ensure they meet preset performance standards and the project is in compliance with the terms of the permits. The compliance monitoring is currently being carried out by L.C. Lee and Associates under contract with the campus institutions. The parameters being monitored are listed in Tables 3 & 4.

Project maintenance is being coordinated by the UWB-CCC campus Physical Plant Service Department.

Appendix 1.

| Some common campus wetland species 2010 |
| --- |
| Growth Form | Species | Common Name |
| Tree | Acer macrophyllum | Big leaf maple |
|  | Alnus rubra | Red alder |
|  | Fraxinus latifolia | Oregon ash |
|  | Malus fusca | Pacific crab apple |
|  | Picea sitchensis | Sitka spruce |
|  | Populus tremuloides | Quaking aspen |
|  | Populus trichocarpa | Black cottonwood |
|  | Psuedotsuga menzeisii | Douglas-fir |
|  | Rhamnus purshiana | Cascara |
|  | Sorbus acuparia * | Rowan tree |
|  | Thuja plicata | Western red cedar |
|  | Tsuga heterophylla | Western hemlock |
| Shrub | Acer circinatum | Vine maple |
|  | Cornus sericea | Red-osier dogwood |
|  | Crategus douglasii | Hawthorn |
|  | Cytisus scoparius * | Scotch broom |
|  | Gaultheria shallon | Salal |
|  | Ledum groenlandicum | Labrador tea |
|  | Lonicera involucrata | Twinberry |
|  | Oemleria cerasiformis | Indian plum |
|  | Physocarpus capitatus | Pacific ninebark |
|  | Ribes sanguineum | Red-flowering currant |
|  | Rosa pisocarpa | Clustered wild rose |
|  | Rubus armeniacus * | Himalayan blackberry |
|  | Rubus laciniatus * | Evergreen blackberry |
|  | Rubus parviflorus | Thimbleberry |
|  | Rubus spectabilis | Salmonberry |
|  | Salix lucida spp. lasiandra | Pacific willow |
|  | Salix scouleriana | Scouler’s willow |
|  | Salix sitchensis | Sitka willow |
|  | Sambucus racemosa | Red elderberry |
|  | Spirea douglasii | Hardhack spirea |
|  | Symphorocarpos albus | Snowberry |
| Herb | Alisma plantago-aquatica | Water-plantain |
|  | Arctium minus * | Common burdock |
|  | Athyerium felix-femina | Lady fern |
|  | Azolla sp. | Duckweed |
|  | Blechnum spicant | Deer fern |
|  | Cardamine oligosperma * | Pepper cress (bitter-cress) |
|  | Cerastium vulgatum | Common chickweed |
|  | Circaea alpina | Enchanter's nightshade |
|  | Cirsium arvense * | Canada thistle |
|  | Cirsium vulgare * | Bull thistle |
|  | Epilobium angustifolium | Fireweed |
|  | Epilobium ciliatum | Purple-leaved willowherb |
|  | Equisetum arvense | Field horesetail |
|  | Equisetum fluvitale | Water horsetail |
|  | Galium trifidum | Small bedstraw |
|  | Geum macrophyllum | Large-leaved avens |
|  | Lotus corniculatus * | Bird’s-foot trefoil |
|  | Lychiton americanum | Skunk cabbage |
|  | Lythrum salicaria* | Purple loosestrife |
|  | Medicago lupulina* | Black medic |
|  | Parentucellia viscosa * | Yellow parentucellia |
|  | Plantago lanceolata | English plantain |
|  | Polygonum cuspidatum* | Japanese knotweed |
|  | Potentilla palustris | Marsh cinquefoil |
|  | Ranunculus repens * | Creeping buttercup |
|  | Rumex crispus* | Curly dock |
|  | Rumex obtusifolius | Bitter dock |
|  | Solanum dulcamara * | Bittersweet nightshade |
|  | Stellaria media * | Common chickweed |
|  | Taraxacum officinale * | Common dandelion |
|  | Trifolium repens * | White clover |
|  | Urtica dioca | Stinging nettles |
|  | Veronica serpyllifolia | Thyme-leaved speedwell |
|  | Vicia americanum | Common vetch |
| Graminoid | Alopecus geniculatus * | Water foxtail |
|  | Anthoxanthum ordoratum * | Sweet vernalgrass |
|  | Carex comosa | Bearded sedge |
|  | Carex deweyana | Dewey’s sedge |
|  | Carex lenticularis | Lenticular sedge |
|  | Carex obnupta | Slough sedge |
|  | Carex rostrata | Beaked sedge |
|  | Carex sitchensis (aquatilis) | Water sedge |
|  | Carex stipata | Sawbeak sedge |
|  | Eleocharis palustris | Creeping spike-rush |
|  | Festuca occidentalis * | Western fescue |
|  | Festuca rubra * | Red fescue |
|  | Holcus lanatus * | Velvet grass |
|  | Juncus acuminatus | Tapertip rush |
|  | Juncus effusus | Common rush |
|  | Juncus ensofolius | Dagger-leaf rush |
|  | Lolium perenne * | Wildrye |
|  | Phalaris arundinacea * | Reed canary grass |
|  | Phleum pratense * | Common timothy |
|  | Poa pratensis * | Kentucky bluegrass |
|  | Scirpus acutus | Threesquare bulrush |
|  | Scirpus lacustris | Softstem bulrush |
|  | Scirpus microcarpus | Small-flowered bulrush |
|  | Typha latifolia | Common cattail |
| * Exotic species |  |  |

# Text boxes

Figure 1.  The North Creek Watershed

Figure 2.  The North Creek Watershed

Figure 3. Campus site and surrounding area in 1871. map taken from General Land Office, U.S. Department of the Interior, Feb. 28, 1884. Based upon a land survey in the Territory of Washington, April 1871.

Campus

North Creek

Figure 4. Land use of campus site prior to campus construction (mid 1990s). Note the straightened stream channel running through farmland and pasture.

Figure 5.  Delineation of jurisdictional wetlands and waters under the 1989 Federal Wetlands Delineation Protocol for the campus site prior to construction. The floodplain shows only intermittent wetland characteristics due to extensive drainage systems and diking. Note especially the hillslope wetlands present in the area of campus construction (dotted line encompasses approximate area of campus building construction).

Figure 6. Campus map showing the pre-construction straightened and diked channel of North Creek and the new meandering primary and secondary channels created by the restoration project.

Straightened channel of North Creek

New meandering channels of North Creek

Figure 7.  Schematic examples of some of the woody debris structures used along the reconstructed channels of North Creek.

I    Fall 1998

II   Fall – Winter 1999

III  Fall 2000

IV  Summer – Fall 2001

V   Future

Figure 8.  Planting phases of the UWB – CCC campus wetland restoration project.

Table 1.  Major species planted within different community types. Also included are major species planted in pits and mounds associated with created microdepressions that are present in all community types. This list groups the 20 planted communities into 5 broad community-type categories and presents only a selected set of common species for each type.

* restricted to peat

Figure 9.  261 Planting polygons of the UWB – CCC campus wetland restoration project.

Figure 10.  Projected physiognomic succession of forested wetland community at the UWB – CCC campus wetland restoration project over the first 25 years.

5 Years

15 Years

25 Years

Table 2.  Major species of animals observed in the UWB-CCC wetlands.

Table 3.  Part I - Compliance monitoring parameters and performance standards for the UWB-CCC restoration project.

Table 4.  Part II - Compliance monitoring parameters and performance standards for the UWB-CCC restoration project.

* species historically recorded in the lower North Creek watershed

UW Bothell – Cascadia Community College Campus

North Creek

Mar 2006

Jun 2003

Oct 2000

Oct 1999

Sept 1998

Central area complete

Planting complete

New channels created

Planting begun

Beginning of construction

Aug 1998

Pre-construction

1997

2006

2001

Figure 11.  Stream bank vegetation development over the first five years.

Project Development 1997 - 2006