Practice Set 2: Answers

1A) 500 billion m.t.C/ 50 billion m.t.C/year = 10 years

1B) 2 billion m.t.C/50 billion m.t.C/year = .04 years or 14.6 days

Terrestrial biomass contains lots of trees and other longer lived organisms.  The woody material in trees means that the carbon gets stored for a longer time.  Ocean biomass is dominated by phytoplankton which does not live or store carbon for a long time.

2A)   Human CO2 emissions = 6 billion mtC/year

Natural CO2 emissions =200 billion m.t.C/year

6 billion m.t.C/year / 200 billion m.t.C/year * 100  = 3.0%

2B)  	Human H2O emissions = 6 billion mt/year (from question)

Natural H2O emissions = 4 x 1020 grams/year   (from class notes/hydro. cycle)

(NEED TO GET THESE INTO SAME UNITS!)

4 x 1020 grams/year  * 1 kg/1000 grams * 1 m.t./1000 kg = 4 x 1014 m.t./year

6 x 109 m.t./year / 4 x 1014 m.t./year * 100   = 1.5 x 10-3 % =  0.0015%

3) For each, you need to assume some daily usage and then calculate the annual usage.

| Item | Watts (typical value) | Daily usage (hrs) | Annual usage (hrs) | Kilowatt hours (per year) | Annual electricity costs ($) |
| --- | --- | --- | --- | --- | --- |
| Refrigerator | 700 | 12 * | 4380 | 3066 | 183.96 |
| Clothes dryer | 1000 | 1 | 365 | 365 | 21.90 |
| Standard light (run continuously) | 75 | 24 | 8760 | 657 | 39.42 |
| Compact fluorescent bulb (run continuously) | 25 | 24 | 8760 | 219 | 13.14 |

* A refrigerator actually only consumes this large amount of electricity when the motor is on.  Typically, this is about half the time the fridge is plugged in.

4A)  Annual savings = $1500 * 0.4 = $600

Payback period = $1000/$600/year = 1.67 years

Annual Return on investment (ROI).  Over 10 years savings = $6000. so:

6000 = 1000 (1+ROI)10 years

To solve this you raise 6000/1000 to the 1/10 power.

Annual ROI = 19.6 %

4B) Energy savings is difference between two models = 450 watts.

Assume refrig motor is on 4380 hours per year so savings

= 450/1000 kw *4380 hrs * $0.06/kwh = $118.26/year

Payback period = $300/$118.26/year = 2.54 years

Return on investment.  Over 10 years savings is $1183

So:   	1183 = 300 (1+ROI)10 years

ROI = 14.7 %