##### Oxidizer (nochromix) Use SOP

University of Washington

| Standard Operating Procedures for Chemicals or Processes |
| --- |
| #1 Process (if applicable) | Oxidizers - use and storage - including the following: (This SOP is not suitable for Perchlorate acid or HF acid.) Nochromix |
| #2 Chemicals | Oxidizers such as dichromates, permanganates, sulfurics, or perchlorates may cause skin irritation or sensitization. Besides these hazardous properties, many oxidizers may present fire and explosion hazards. |
| #3 Personal Protective Equipment (PPE) | Wear chemical splash gloves and heavy duty nitrile or neoprene gloves. Call EH&S (3-0467) for further information if needed. A lab coat or apron is recommended for personal protection and is required when dispensing or cleaning up a spill of a quantity greater than 1 liter of liquid or 0.5 kg of a solid. |
| #4 Environmental / Ventilation Controls | Volatile oxidizers should be dispensed in a fume hood. |
| #5 Special Handling Procedures & Storage Requirements | Store separate from organic compounds, flammable materials, metals, and other easily oxidizable materials; do not use metal containers. Do not use metal containers for oxidizer storage. Storage location: BAG 023, in packets on the chemical shelf. |
| #6 Spill and Accident Procedures | Absorb a liquid spill with suitable diatomaceous earth or universal spill pads, except for concentrated nitric acid. Neutralize concentrated nitric acid with copious amounts of baking soda. Place used absorbent materials in plastic containers. |
| #7 Waste Disposal | Label with Hazardous Waste Label, accumulate according to requirements, and send in Chemical Collection Request or Routine Pickup request, both available online at http://www.ehs.washington.edu/epowaste/chemwaste.shtm. |
| #8 Special Precautions for Animal Use (if applicable) | * |
| Particularly hazardous substance involved? | YES: | Blocks #9 to #11 are Mandatory |
|  | X NO: | Blocks #9 to #11 are Optional. |
| #9 Approval Required | N/A |
| #10 Decontamination | N/A |
| #11 Designated Area | N/A |
| Name: Sarah Keller Title: PI |
| Signature: Date: July 21, 2014 |

Environmental Health and Safety, Box 354400			*to be filled in by PI or Supervisor